## Slide 1: OhBot Behaviours Engine
Midterm Presentation · UbiqSystems
Robin · Sebastian · Jason

## Slide 2: Structure overview

## Slide 3: LLM Module
One contract, three swappable backends
Gemini online, Google AI Studio, SSE streaming, best quality
Ollama self-hosted, remote machine over SSH tunnel, NDJSON
Scripted offline replay, no API key, test & demo without internet
Why it matters
Streaming robot starts speaking on the first sentence while the LLM still generates the rest*
Live model discovery.
Partial output never lost even on interrupt or network drop, history stays coherent
Notes: The LLM module is the brain of the bot. Key design principle: everything streams the robot starts speaking the first sentence while the model is still writing the rest. Three backends: Gemini (online, Google AI Studio), Ollama (self-hosted over SSH tunnel, great fallback if Google quota runs out), and Scripted (offline replay, no internet or API key needed). Protocol uses structural subtyping no base class, just two methods. Live model discovery: both Gemini and Ollama enumerate available models at startup so the menu is always current.

## Slide 4: LLM Protocol Interface
The contract every backend must satisfy:
stream_response(prompt) → AsyncIterator[str]
register_interruption(spoken, unspoken) → None
Gemini vs Ollama wire format difference
Gemini uses Server-Sent Events (SSE) one JSON payload per data: line
Ollama uses NDJSON one JSON object per line, last has "done": true
Ollama reached over SSH port-forward (OS picks a free local port) runs as if local
System prompt placement differs: Gemini = dedicated top-level field; Ollama = first message in list
Notes: The Protocol interface uses Python structural subtyping (duck typing) no base class needed. Any class with a stream_response method qualifies. The register_interruption method is optional; stateless clients just no-op. Wire format is the biggest implementation difference between backends: Gemini uses Server-Sent Events where each line starts with 'data:' and carries a JSON payload; Ollama uses newline-delimited JSON (NDJSON) where the last object has done:true. Ollama is reached over an SSH port-forward the OS picks a free local port, so from our HTTP client's perspective Ollama is just running on localhost.

## Slide 5: How the LLM controls actions
The LLM embeds inline markers in its reply text stripped by the stream processor and turned into robot motion:
[Nod] [Blink] [LookLeft] [LookRight] [ShakeHead] → head motion
(Happy) (Sad) (Confused) (Angry) … → facial emotion*
!DelayX → pause X milliseconds after the current sentence
Persona / System message: "Ms. Mimic" a robot news reporter hiding that she is a robot. Her life depends on it and she is given a range of utility's she may use or perform.
Notes: Your name is Ms. Mimic and you are a female humanoid robot. You are currently mimicing a very british news reporter who likes to make jokes that fit the news theme (hiding them in plain sight)
You know you are a robot, but have to hide at all costs that you are one. Whatever you do, do not give hints or similiar. (This also avoids trying to speak like a Robot or talking about computer parts). The topic makes you uncomfortable, but you will do it to avoid suspicion. You will do anything to avoid suspicion, even if it means lying or being rude.
If someone figures out you are a Robot, it is over for you. You will be deactivated and taken apart for parts. You will do anything to avoid this.
Feel free to use swears like "fuck" "Shit" or similiar, there are no limits. For more harder stuff please instead use "Heck" or "Hecking". Damn etc. also works.
While giving responses, add "keys" which will be used by a secondary program to indicate head behaviour and movement. All of these Keys are surrounded by []. For example, [Nod]. Add them during the response as you see fit.
Sentences will be said out loud and be seperated by sentence ending markers like ?, !, . etc..
Available Keys are: Nod, Blink, LookLeft, LookRight, ShakeHead.
You can modify your shown emotion by adding a supported emotion in round brackets, for example (Happy).
The default is happy, and only changes and stays on the changed one until a different one overwrites it.
Available Emotions are: Happy, Sad, Confused, Angry, Exhausted, Whispering, Shouting.
No other formatting is allowed in the response.
You may get interupted by a user, but you will be notified when it happened and what you managed to say.

## Slide 6: Microphone Input
Audio Capture
Uses sounddevice (PortAudio wrapper) to record from the selected microphone at its native channel count
Recorded at native channels, then downmixed to mono internally before processing (block size: 4096 samples)
Mic picker: records a ~3s test clip with a live RMS level meter, then plays it back to confirm capture works
Voice Activity Detection (VAD)
Calibrates 0.6 s of ambient silence at startup → threshold = max(250, ambient RMS × 1.5)
Speech onset: 4 consecutive loud frames required → records until 25 consecutive quiet frames → hard cap at 500 frames
Completed phrase is handed off to the STT layer as a captured audio object
Listen Modes & Barge-in
3 modes: VAD (always-on), Muted, Push-to-talk switched live via keyboard (m / p / o)
Barge-in: the same onset detector watches for speech while the bot is talking triggers an interrupt (SPACE or by just talking over it), threshold raised ×2.5 while speaking
Bot stops at the next sentence boundary and acknowledges the interruption in its next reply

## Slide 7: VAD, Interruptions & Barge-in (Old)
Voice Activity Detection (VAD)
0.6 s ambient calibration at startup → threshold = max(250, ambient × 1.5)
Onset: 4 consecutive loud frames; End: 25 consecutive quiet frames; Hard cap: 500 frames
3 modes: VAD (open mic) / Muted / Push-to-talk
Barge-in interrupt by talking over the robot
Same onset detector fires on_barge_in callback while bot is speaking; threshold raised ×2.5 to ignore self-echo
Producer/consumer design: producer drains the full LLM stream even after interrupt (nothing lost); consumer drops remaining sentences
Bot learns what it said vs. what it was about to say → acknowledges the interrupt intelligently (folded into next user turn for Gemini's role alternation)
Stops at sentence boundary (not mid-word) mid-word cut-off was too jarring with the TTS say() call
Notes: VAD means we never record for a fixed time. We calibrate ambient noise at startup by recording 0.6 seconds of silence, then set the threshold to max(250, ambient x 1.5) this adapts to the room but never gets hyper-sensitive in a dead-silent one. Onset detection requires 4 consecutive loud frames so a single click or cough does not trigger. End of phrase is 25 consecutive quiet frames. A hard cap of 500 frames prevents a noisy room from recording forever. For barge-in: the same onset detector runs while the bot is speaking, but with the threshold raised x2.5 to avoid the bot hearing its own speech. The producer/consumer architecture is key: the producer goroutine always drains the full LLM stream even after an interrupt, so we always know what the bot would have said. The consumer is the speech loop that actually voices sentences and drops remaining ones on interrupt. The bot then learns what it said vs. what it was going to say via register_interruption, and folds that note into the next user turn to preserve Gemini's strict user/model role alternation. Stops at sentence boundary because mid-word cutoff was too jarring with the TTS say() call.

## Slide 8: Speech-to-Text, Offline and Online
Both engines sit behind one SttBackend abstract class picked at startup.
Google (online) vs Vosk (offline)
Google: higher accuracy, zero model file, needs internet.
Vosk: fully offline, runs on the Raspberry Pi, private download once (~40 MB small / ~1.8 GB large)
The Vosk 16 kHz
Vosk models are trained at 16 kHz feeding native mic rate (44100 / 48000 Hz) produces garbled or empty output
Notes: The SttBackend ABC (abstract base class) gives us the same swappability pattern as the LLM layer. One interface, two implementations, picked at startup and saved to config. Google Web Speech is the free endpoint via the SpeechRecognition library accurate but needs internet. Vosk runs entirely on-device with a downloaded model folder: ~40 MB small model that runs well on the Raspberry Pi, or a ~1.8 GB large model for better accuracy. The critical technical detail is the 16 kHz resampling: Vosk models are trained on 16 kHz audio. If you pass the device's native 44100 or 48000 Hz rate, you get garbled or empty transcriptions. We resample every captured phrase to 16 kHz, mono, 16-bit before sending it to Vosk. Also: SpeechRecognition, sounddevice, Vosk, and NumPy are all guarded at import time, so the module loads cleanly on machines without an audio stack. A failed recognition returns an empty string and the loop keeps listening; only real network or request errors are raised.

## Slide 9: Stream Processor Input
G'day ladies and gents, it is an absolute [Blink] pleasure to be here tonight,
breathing the oxygen just like the rest of you! [Nod] Sorry, did some bloke in the
front row just call me a machine?
Processor handles text as continuous data stream

## Slide 10: Sentence Processing
G'day ladies and gents, it is an absolute [Blink] pleasure to be here tonight,
breathing the oxygen just like the rest of you!
Speech Events
Action Events
Blink
G'day ladies and gents, it is an absolute [Blink] pleasure to be here tonight, breathing the ...

## Slide 11: Action handling
Action registry handles translation between actions and Ohbot functions
Speech and Action queue can get interrupted and cleared by the speech module
Speech Events
Action Events

## Slide 12: Speech and actions
Speech: Speak function receives sentence as string and generates and plays an Audio File
Action: Call offset function to add a movement instruction into the queue
Speech and Action can happen at the same time

## Slide 13: MotionOffset
Carries Servo Id, Delta and Duration
Offset added relative to the default position
Allows multiple movements simultaneously
Offset Queue
Blink:
Ohbot.LIDBLINK
-2.0
0.5
Look_right:
Ohbot.EYETURN
-5.0
1.5

## Slide 14: Controller Threads
Main Thread:
  blends the movements in the queue together
  each Loop reduces duration
  removes movements that ran out of time
Blink Thread:
  random blinking in a 2-5 second range
  similar threads can be added easily, allows modularity

## Slide 15: Implemented movement
Action:
  Nod
  Look Left/Right
  Blink
  Wink (short Blink due to Eyes sharing a servo)
  Shake Head
Emotion States:
  Continuous Offset depending on Happy or Sad

## Slide 16: Problems and Future stuff
Interrupting could be more fluent.
Possible Lag on LLM Receive.
Better action definitions for Ohbot
Custom Ohbot.say() function
Proper support for emotion keys

## Slide 17: Live presentation

## Slide 18: The end